# Accumulation Radar

## Summary

The Accumulation Radar data set contains L1B Geolocated Radar Echo Strength Profiles over Greenland, Canada, and Antarctica taken with the CReSIS Radar Depth Sounders (RDS).

The L1B data set includes measurements for echograms, time, latitude, longitude, elevation, as well as flight path charts and echogram images.

The accumulation radar data have been collected on an ongoing basis since 1999 using grant funding from NASA and NSF. The most recent data were collected as part of the NSF Science and Technology Center grant (ANT-0424589) and the NASA Operation IceBridge field campaign (NNX10AT68G).

The data are stored in MATrix LABoratory (MATLAB) files with associated JPG, CSV, and PNG files.

The data are available at ftp://ftp.cresis.ku.edu/ and http://ftp.cresis.ku.edu/. These two sites serve the same data, but use the ftp (port 21) and http (port 80) protocols respectively.

## FAQ

The most convenient way to browse the imagery quickly is through the JPG files in the images directory.

The quickest way to plot the whole dataset is to look at the browse files (KML or CSV) for the whole season in the csv directory (csv).

The standard L1B files are in the CSARP_qlook directory. These are located in ftp://ftp.cresis.ku.edu/snow/{$season_name}/.

For the highest quality and most complete browsing of the data, use the Matlab image browser at ftp://ftp.cresis.ku.edu/picker/. The guide for the picker also explains the picking process.

Mathworks MAT file readers for C and IDL including documentation from Mathworks are located at ftp://ftp.cresis.ku.edu/mat_reader/.

## Data Organization

The radar data are divided into segments. A segment is a contiguous dataset where the radar settings do not change. A day is divided into segments if the radar settings were changed, hard drives were switched, or other operational constraints required that the radar recording be turned off and on. The segment ID is YYYYMMDD_SS where YYYY is the 4-digit year (e.g. 2011), MM is the 2-digit month from 1 to 12, DD is the 2-digit day of the month from 1 to 31, and SS is the segment number from 0 to 99. Segments are always sorted in the order in which the data was collected. Generally SS starts with 1 and increments by 1 for each new segment, but this is not always the case: only the ordering is guaranteed.

Each segment is broken into frames (analogous to satellite SAR scenes) to make analyzing the data easier. Most frames are 2-3 km long. Currently frames are aligned with raw data files (frame number matches raw file index), but this may not always be the case for future missions. Once the frame boundaries are defined, they will not change from one release to the next or one processing method to the next.  The frame ID is a concatenation of the segment ID and a frame number and follows the format YYYYMMDD_SS_FFF where FFF is the frame number from 000 to 999. Generally the FFF starts with 0 or 1 and increments by 1 for each new frame, but this is not always the case: only the ordering is guaranteed.

In a data casting sense, the data granule for L1B data is the frame.

## File Descriptions

On the ftp.cresis.ku.edu/accum page, L1B are in the accumulation radar folder (accum), arranged by Season ID (e.g. 2011_Greenland_P3). Since L1B files are specific to a season and contain only accumulation radar data, these files are stored together in the season ID folders under the directory snow.

### L1B products

#### CSARP_{$processing_type}/{$segment_id}/Data{$image_id}_{$frame_id}.mat

For each data frame there may be many different L1B products depending on how waveforms, and channels are combined and how the processing is done. More details about the standard outputs are given in the Methods section. An example filename is:

CSARP_qlook/20110516_01/Data_0110516_01_006.mat

The {$processing_type} is a string. Currently the only processing type is qlook.

The {$segment_id} is explained in the Data Organization section.

The {$image_id} is a string which is always empty at this point.

The {$frame_id} is explained in the Data Organization section.

The file format is Matlab .MAT version 6.

#### images/{$segment_id}/{$frame_id}_HHmmSS_{0maps,1echo}.jpg

For each data frame there is a flight path file (0map) and an echogram file (1echo). The background images for 1) sea ice flights are the Bremen sea ice concentration maps in the projection that is used by the Geotiff’s from this site, or 2) Landsat-7 natural color imagery in polar stereographic format (70 deg true scale latitude, -45 deg longitude is center for Greenland/Canada and -71 deg true scale latitude, 0 deg longitude is center for Antarctica). A few example filenames are:

images/20110507_01/20110507_01_001_110941_0maps.jpg

images/20110507_01/20110507_01_001_110941_1echo.jpg

HHmmSS is the GPS time stamp for the first range line in the image where HH is 00-23 hours, mm is 00-59 minutes, and SS is 00-59 seconds.

The echograms are generated from the qlook data product.

The file format is JPEG.

### L2 products

#### csv/{$segment_id}/Data_{$frame_id}_HHmmSS.csv

FILES NOT CURRENTLY AVAILABLE.

Contains the ice surface and layering information. There is one file per data frame. An example filename is:

csv/20110407_06/Data_20110407_06_001_151055.csv

HHmmSS is the GPS time stamp for the first range line in the csv file where HH is 00-23 hours, mm is 00-59 minutes, and SS is 00-59 seconds.

The file format is comma separated variable (CSV).

#### csv/Data_{$segment_id}.csv

FILES NOT CURRENTLY AVAILABLE.

These files are provided for ease of download and file transfer. They are the same format as the individual data frame CSV files. These files have all the individual frames from the segment concatenated together. An example filename is

csv/Data_20110331_09.csv

#### csv/{$season_id}.csv

FILES NOT CURRENTLY AVAILABLE.

These files are provided for ease of download and file transfer. They are the same format as the individual data frame CSV files. These files have all the individual frames from the whole season concatenated together.

The {$season_id} is a string that is formatted as YYYY_location_platform, YYYY is the 4-digit year of when the season began, location is the geographic location (e.g. Greenland or Antarctica), and platform is the airborne system used (e.g. P3, TO, DC8, Ground).

An example filename is:

csv/2011_Greenland_P3.csv

#### csv/Browse_Data_{$segment_id}.csv

The save as the segment CSV file except only the first point is taken from each frame to keep the file size small.

csv/Browse_Data_20110331_09.csv

#### layerData/{$segment_id}/Data_{$frame_id}.mat

For each data frame there is a layer data file. This file contains the full layer information for the ice surface and any other layers that have been picked and is required by the image browser/layer picker. An example filename is:

CSARP_layerData/20110516_01/Data_20110516_01_006.mat

The file format is Matlab .MAT version 6.

### Browsing Files

#### kml/Browse_Data_{$segment_id}.kml

KML versions of the segment browsing CSV files.

#### {$radar_id}_param_{$season_id}.xls

This spreadsheet file allows all of the radar and processing parameters to be browsed conveniently. These parameters are encapsulated in the L1B data files, but this spreadsheet provides another way to access this information. An example filename is:

accum_param_2011_Greenland_P3.xls

The {$radar_id} is a string containing the radar ID which is one of icards, mcrds, mcords, or mcords2.

### General utilities and documents

ftp://ftp.cresis.ku.edu/gps_ins/

See guide in this folder for more details. The individual GPS/INS files are stored with this naming convention:

{$season_id}/gps_YYYYMMDD.mat

A few examples are:

2011_Greenland_P3/gps_20110507.mat

2011_Greenland_P3/gps_20110516.mat

The file format is Matlab .MAT version 6.

ftp://ftp.cresis.ku.edu/matlab_MAT_reader/

Matlab MAT file reader for Matlab, C, and IDL. See guide in this folder for more details.

ftp://ftp.cresis.ku.edu/picker/

Echogram browsing tool (currently requires Matlab). See guide in this folder for more details

ftp://ftp.cresis.ku.edu/loader/

Echogram loader tool (currently requires Matlab). See guide in this folder for more details. This tool has not been released yet.

ftp://ftp.cresis.ku.edu/segy/

SEGY and SEG2 converter tool (currently requires Matlab). See guide in this folder for more details. This tool has not been released yet.

ftp://ftp.cresis.ku.edu/rds/accum_readme.doc

The most recent version of this readme file.

### L1B Matlab Files

Data filenames start with “Data_” followed by the frame ID.

- Data_20091224_01_001.mat

Each Matlab (.mat) file has the following variables:

| Name | Data |
| --- | --- |
| Size/Axes | M by N single array where M is fast time and N is slow time |
| Units | Relative received power (Watts) |
| Range | Full single range |
| Null Value | 0 |
| Description | Radar echogram data. |

| Name | Time |
| --- | --- |
| Size/Axes | M by 1 double vector where M is fast time |
| Units | Seconds |
| Range | Full double range |
| Null Value | NA |
| Description | Fast time (zero time is the beginning of the transmit event calibrated to within one range resolution cell) |

| Name | GPS_time |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Seconds |
| Range | Full double range |
| Null Value | NA |
| Description | GPS time when data were collected (seconds since Jan 1, 1970 00:00:00). This is the ANSI C standard. |

| Name | Latitude |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Degrees |
| Range | -90 to +90 |
| Null Value | Not a Number (indicates that no GPS information is available) |
| Description | WGS-84 geodetic latitude coordinate. Always referenced to North. Represents the location of the origin of the trajectory data which is generally not the radar’s phase center, but some other point on the aircraft (e.g. the GPS antenna or the INS). |

| Name | Longitude |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Degrees |
| Range | -180 to +180 |
| Null Value | Not a Number (indicates that no GPS information is available) |
| Description | WGS-84 geodetic longitude coordinate. Always referenced to East. Represents the location of the origin of the trajectory data which is generally not the radar’s phase center, but some other point on the aircraft (e.g. the GPS antenna or the INS). |

| Name | Elevation |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Meters |
| Range | Full double range |
| Null Value | Not a Number (indicates that no GPS information is available) |
| Description | Referenced to WGS-84 ellipsoid. Positive is outward from the center of the Earth. Represents the location of the origin of the trajectory data which is generally not the radar’s phase center, but some other point on the aircraft (e.g. the GPS antenna or the INS). |

| Name | Surface |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Seconds |
| Range | Full double range |
| Null Value | Not a Number (indicates that no surface information is available) |
| Description | Estimated two way propagation time to the surface from the collection platform. This uses the same frame of reference as the Time variable. |

| Name | *param* (multiple variables with a name containing the string “param”) |
| --- | --- |
| Size/Axes | NA, data structures |
| Units | NA |
| Range | NA |
| Null Value | NA |
| Description | Contains: 1) Radar and processing settings, 2) Processing software version and time stamp information. Fields of structures are not static and may change from one version to the next. |

### L2 Matlab Files

| Name | GPS_time |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Seconds |
| Range | Full double range |
| Null Value | NA |
| Description | GPS time when data were collected (seconds since Jan 1, 1970 00:00:00). This is the ANSI C standard. |

| Name | Latitude |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Degrees |
| Range | -90 to +90 |
| Null Value | Not a Number (indicates that no GPS information is available) |
| Description | WGS-84 geodetic latitude coordinate. Always referenced to North. Represents the location of the radar echogram data phase center. It may not be the actual measurement location due to motion compensation |

| Name | Longitude |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Degrees |
| Range | -180 to +180 |
| Null Value | Not a Number (indicates that no GPS information is available) |
| Description | WGS-84 geodetic longitude coordinate. Always referenced to East. Represents the location of the radar echogram data phase center. It may not be the actual measurement location due to motion compensation |

| Name | Elevation |
| --- | --- |
| Size/Axes | 1 by N double vector where N is slow time |
| Units | Meters |
| Range | Full double range |
| Null Value | Not a Number (indicates that no GPS information is available) |
| Description | Referenced to WGS-84 ellipsoid. Positive is outward from the center of the Earth. Represents the location of the radar echogram data phase center. It may not be the actual measurement location due to motion compensation |

| Name | layerData |
| --- | --- |
| Size/Axes | 1 x P cell array of structures, where P is the number of layers |
| Units | NA |
| Range | NA |
| Null Value | NA |
| Description | The first layer (layer_idx = 1) is the ice surface. |

| Name | layerData{layer_idx}.name |
| --- | --- |
| Size/Axes | character array, arbitrary length |
| Units | NA |
| Range | NA |
| Null Value | NA |
| Description | Name of the layer (“surface” is reserved for ice surface) |

| Name | layerData{layer_idx}. value |
| --- | --- |
| Size/Axes | 1 by 2 cell array of structures |
| Units | NA |
| Range | NA |
| Null Value | NA |
| Description | First entry contains manually entered points for this layer, second entry contains automatically generated layer information |

| Name | layerData{ layer_idx}.value{pick_idx}.data |
| --- | --- |
| Size/Axes | 1 by N double vector |
| Units | Seconds |
| Range | Full double range |
| Null Value | Not a Number (indicates that no surface information is available for this particular index and pick type) |
| Description | Estimated two way propagation time to the surface from the collection platform. There are two pick types: the manual picks are stored in pick_idx = 1 and the automated picks are stored in pick_idx = 2. |

| Name | layerData{ layer_idx}.quality |
| --- | --- |
| Size/Axes | 1 by N double vector |
| Units | NA |
| Range | 1, 2, or 3 |
| Null Value | NA |
| Description | Quality level of the data (1-3), 1 represents high confidence, 2 represents low confidence or large error bars, and 3 represents a derived or estimated result based on information beyond just the present data frame |

## Theory of Measurements:

The radar architecture is a combined stepped-chirped system. The complete bandwidth from 565 to 885 MHz is divided into 16 overlapping subbands (550-600, 570-620, …, 850-900). Data is recorded on each subband. In post processing, the subbands are combined into a single frequency band. The accumulation radar is only installed on the P-3 using an antenna installed in the bomb bay.

### Radar System

The following table lists the nominal properties of the radar system.

|  | Frequency Spectrum (MHz) | Pulse Duration (µs) | Transmit Power (W) | Noise Figure (dB) | Antenna Beamwidth Along x Cross (deg) |
| --- | --- | --- | --- | --- | --- |
| 2009 Antarctica TO |  |  |  |  |  |
| 2010 Greenland P3 |  |  |  |  |  |
| 2011 Greenland TO |  |  |  |  |  |
| 2011 Greenland P3 | 550-900 | 2 |  |  | 21 x 18 |

|  | Pulse Repetition Frequency (Hz) | Hardware Averages |
| --- | --- | --- |
| 2009 Antarctica TO |  |  |
| 2010 Greenland P3 |  |  |
| 2011 Greenland TO |  |  |
| 2011 Greenland P3 | 50000 | 16 |

## L1B Processing Steps:

The following processing steps are performed.

- Conversion from quantization to voltage at the 50 ohm antenna

- Removal of DC-bias by subtracting the mean from each record

- Channel compensation between each of the 16 subbands. This includes amplitude mismatches only.

- Pulse compression with time domain window which matches transmitted time domain window and an additional frequency domain window

- Sixteen subbands are combined into a single band.

- The quick look output is generated using presumming or unfocused SAR processing for a total of 160 coherent averages which includes hardware and software averages.

- A 1 range-bin by 10 along-track-range-line boxcar filter is applied to the power detected data and then decimated in along-track by 5.

- The quick look output is used to find the ice surface location (fully automated).

## Resolution and Error Bounds

For a flat surface, the range resolution is:

where = 320 MHz is the bandwidth (565 to 885 MHz),  is the index of refraction for the medium,  is the speed of light in a vacuum, and = 1.5 is due to the application of a hanning time-domain window to reduce the range sidelobes of the chirped transmit waveform. The range resolution for several indices of refraction is given in this table.

| Index of Refraction | Range Resolution (m) | Medium |
| --- | --- | --- |
| 1 | 0.70 | Air |
| sqrt(2.0) | 0.50 | Snow |
| sqrt(3.15) | 0.40 | Solid ice |

The index of refraction can be approximated by  where  is the density of the snow in grams per cm3. In the data posting, a dielectric of 2.0 is used which corresponds to a snow density of 0.51 g per cm3.

The antenna installed in the bomb bay of the P-3 is a 2 by 4 element antenna array where each element is an elliptical dipole and the array is aligned so that there are 2 elements in the along-track direction and 4 elements in the cross-track direction. The dipoles are aligned with the fuselage so that the E-plane is along-track. The element spacing is 26 cm in cross-track and 37 cm in along-track. The approximate beamwidths are 21 deg in along-track and 18 deg in cross-track. The footprint is a function of range

where  is the beamwidth in radians and  is the height above ground level. For  = 500 m, the footprint is 185 m in along-track and 158 m in cross-track.

For a smooth target (e.g. internal layers), the primary response is from the first Fresnel zone which is considerably smaller than the antenna footprint. The first Fresnel zone is a circle with diameter given by

where  = 0.4 m is the wavelength at the center frequency. For  = 500 m, the diameter is 20 m.

For a rough surface with no appreciable layover, the cross-track resolution will be constrained by the pulse-limited footprint, which is approximately

where  is the height above the air/ice interface and  is the ice thickness.

For  = 500 m, the cross-track resolution is 54.8 m.

In the along-track dimension, data are coherently averaged 160 times which includes both hardware and software averaging,and decimated by this same amount so that the along-track spacing between records with a platform speed of 140 m/s is 7.2 m. A 1 range-bin by 10 along-track-range-line boxcar filter is applied to the power detected data and then decimated in the along-track by 5 so the data product has an along-track resolution of 35.8 m.

## Season Specific Information

### 2009 Antarctica TO

Not completed

### 2010 Greenland P3

Not completed

### 2011 Greenland TO

Not completed

### 2011 Greenland P3

#### Known Issues

The accum, snow, and kuband data acquisition systems have a known issue with radar data synchronization with GPS time. When the radar system is initially turned on, the radar system acquires UTC time from the GPS NMEA string. If this is done too soon after the GPS receiver has been turned on, the NMEA string sometimes returns GPS time rather than UTC time. GPS time is 15 seconds ahead of UTC time during this field season. The corrections for the whole day must include the offset (-15 second correction). GPS corrections have been applied to all of the data using a comparison between the accumulation, snow, and kuband radars which all have independent GPS receivers. A comparison to geographic features and between ocean surface radar return and GPS elevation is also made to ensure GPS synchronization. GPS time corrections are given in the vector worksheet of the parameter spreadsheet. This issue is closed.

The data are not radiometrically calibrated. This means that they are not converted to some absolute standard for reflectivity or backscattering analysis. We are working on data processing and hardware modifications to do this.

The data have not been elevation compensated. Elevation compensation must be applied after loading the data and example is given below. This issue is closed.

#### Coverage

Not completed

#### Field Team

Principle Investigator: Carl Leuschen

Radar Installation: Reid Crowe, Carl Leuschen, Cameron Lewis, Ben Panzer, Kevin Player, Fernando Rodriguez-Morales

Radar Operation: Austin Arnett, Carl Leuschen, John Paden, Ben Panzer, Kevin Player

Data Processing: John Paden
Data Backups and IT: Dan Hellebust, Justin Miller

Post Data Processing (for this release): Aric Beaver, John Paden

## Acknowledgement and Citing the Data:

Whenever the data is used, please include the following acknowledgement:

We acknowledge the use of data and/or data products from CReSIS generated with support from NSF grant ANT-0424589 and NASA grant NNX10AT68G.

Please cite data according to NSIDC standard.

Leuschen, Carl, Cameron Lewis, Prasad Gogineni, Fernando Rodriguez, John Paden, Jilu Li. 2011, updated current year. IceBridge Accumulation Radar L1B Geolocated Radar Echo Strength Profiles, [list dates of data used]. Boulder, Colorado USA: National Snow and Ice Data Center. Digital media.

## References and Related Publications

CReSIS Website (https://www.cresis.ku.edu/).

IceBridge Data Web site at NSIDC (http://nsidc.org/data/icebridge/index.html).

IceBridge Web site at NASA (http://www.nasa.gov/mission_pages/icebridge/index.html).

ICESat/GLAS Web site at NASA Wallops Flight Facility (http://glas.wff.nasa.gov/).

ICESat/GLAS Web site at NSIDC (http://nsidc.org/daac/projects/lidar/glas.html).

Lewis, C., "Airborne UHF Radar for Fine Resolution Mapping of Near Surface Accumulation Layers in Greenland and West Antarctica", Department of Electrical Engineering and Computer Science: Master's Thesis, University of Kansas, 12/2010.

Lewis, C.; Patel, A.; Owen, H.; Rodriguez-Morales, F.; Leuschen, C.; Seguin, S.A.; Ledford, J.; Player, K.; Gogineni, S.; , "A radar suite for ice sheet accumulation measurements and near-surface internal layer mapping," Geoscience and Remote Sensing Symposium,2009 IEEE International,IGARSS 2009 , vol.5, no., pp.V-441-V-444, 12-17 July 2009
doi: 10.1109/IGARSS.2009.5417635

Rodriguez-Morales, F., P. Gogineni, C. Leuschen, C. T. Allen, C. Lewis, A. Patel, L. Shi, W. Blake, B. Panzer, K. Byers, R. Crowe, L. Smith, and C. Gifford, Development of a Multi-Frequency Airborne Radar Instrumentation Package for Ice Sheet Mapping and Imaging, Proc.  2010 IEEE Int. Microwave Symp., Anaheim, CA,  May 2010, pp. 157 – 160.

## Contacts

Please send all questions and comments to:

cresis_data@cresis.ku.edu