GPS File Format

Uses the Matlab –v6 file format (if files are –v7 or compressed, then please notify us and we will update them).

See matlab_format.pdf file from Mathworks.

Contents of file:

| Variable Name | Type | Size | Units | description |
| --- | --- | --- | --- | --- |
| gps_time | double | 1xN | sec | Time in seconds since the Jan 1, 1970 epoch (i.e. ANSI C standard) |
| lat | double | 1xN | deg | Geodetic latitude in degrees north referenced to WGS-84 ellipsoid |
| lon | double | 1xN | deg | Geodetic longitude in degrees east referenced to WGS-84 ellipsoid |
| elev | double | 1xN | deg | Elevation in meters referenced to WGS-84 ellipsoid |
| roll | double | 1xN | rad | Standard aircraft measurement, positive roll is right wing tipping down |
| pitch | double | 1xN | rad | Standard aircraft measurement, positive pitch is nose of aircraft tipping upward |
| heading | double | 1xN | rad | Standard aircraft measurement, heading is relative to north with positive heading east |
| gps_source | char | variable | NA | A string describing the source of the data. This field is not always available. |

Typically, we desire  to know the trajectory of the phase center of each antenna element. To find that, you must know the lever arm between the GPS file’s origin and the antenna element in the standard aircraft body coordinate system (X points out nose of aircraft, Y points to right wing, Z points down). Each season may have one or more possible sources and you must have the documentation for each source to determine this lever arm. This is provided with the README for each dataset.