## Slide 1: Polar Format Algorithm SAR Processor
  Follows (then extends for z-dimension):
  Armin W. Doerry, Synthetic Aperture Radar Processing with Tiered Subapertures, Sandia Report SAND94-1390, 1994.
  PFA originally developed by:
  Jack L. Walker, "Range-Doppler Imaging of Rotating Objects," Ph.D. dissertation, University of Michigan, Ann Arbor, MI, 1974.
  Jack L. Walker, Range-Doppler Imaging of Rotating Objects, IEEE Transactions on Aerospace and Electronic Systems, vol. 16, no. 1, Jan 1980.

## Slide 2: Deramp on Receive

## Slide 3: Deramp on Receive

## Slide 4: Deramp on Receive
How do we create a frequency shift?
Complex exponential
How do we create the specific frequency shift versus time along the dashed “reference/scene-center” that we need here?
A chirp!

## Slide 5: Deramp on Receive
Recall our time-space signal formula for a point target:
Consider just the azimuth carrier term . Let’s compute the instantaneous phase and frequency functions as a function of :

## Slide 6: Deramp on Receive
Copying result from previous slide:
When , then and it is a linear frequency ramp
When , then  asymptotically approaches constant frequencies of (positive on the approach to the target and negative after passing the target)
Remember max Nyquist sampling is !

## Slide 7: Deramp on receive
Deramping spotlight SAR keeps the instantaneous bandwidth in both time and space small
  This is great for spotlight SAR where the time-gate (time-window) and the Doppler-gate (Doppler bandwidth) are restricted
Deramping is also a fundamental/first step of the polar format algorithm.

## Slide 8: Deramp on Receive
Recall our time-space signal formula for a point target:
Multiplication by a delayed chirp to deramp
Replace window with one centered on the scene center:
(hidden dependence to make it easier to read/write)
Define

## Slide 9: Deramp…
Ignore residual video phase term since it has no time dependence and we just have a frequency tone at !!!
Deramp the azimuth carrier phase term:
Assume spotlight antenna beam highlights targets for entire collection
Combine both deramp results:
Replace dependence with  Why does this make sense?

## Slide 10: Deramp on Receive
Copying result from previous slide
Hmmm……………………. what does this look like? Frequency domain of pulse compressed signal!
Let’s take a closer look at . Each term is a hyperbola as a function of slow-time . is the fixed hyperbola for the scene center. is the hyperbola for an arbitrary point target.
If we ignore changes in the spherical curvature between and , we can approximate .

## Slide 11: Deramp on Receive

## Slide 12: Deramp on Receive

## Slide 13: Deramp on Receive
So just like with f-k migration:
  We can manipulate the analytical form into the 2D Fourier transform of the SAR image .
  The sampling is not uniform in or in the case of the polar format algorithm so IDFT2 is not possible
  What can we do? 2D sinc-interpolation to a uniform grid!

## Slide 14: After deramping, and samples:
Notes:   Armin W. Doerry, Synthetic Aperture Radar Processing with Tiered Subapertures, Sandia Report SAND94-1390, 1994.

## Slide 15: After resampling, and samples:
Notes: Armin W. Doerry, Synthetic Aperture Radar Processing with Tiered Subapertures, Sandia Report SAND94-1390, 1994.

## Slide 16: After resampling, and samples: (and now we are ready to apply IFFT2!)
Notes: Armin W. Doerry, Synthetic Aperture Radar Processing with Tiered Subapertures, Sandia Report SAND94-1390, 1994.

## Slide 17: Polar Format Algorithm: Resampling (connection to Doerry’s publication)
Data are sampled at along-track samples, , and range samples, which are related to the wavenumber domain as:
  where in Doerry’s overview
With PFA, we will implement a 1D interpolation in range to these samples which result in uniform sampling in around the center frequency:
  where in Doerry’s overview.
The values of to sample at are generally chosen to cover the same wavenumber domain extent as the original data samples. To determine these values, , is solved for in terms of the minimum and maximum values across all range lines.
Once the extent of integer samples is determined, we find the that corresponds to each. Continued…

## Slide 18: Polar Format Algorithm: Resampling (connection to Doerry’s publication)
We want to find the such that:
Solving for :

## Slide 19: Polar Format Algorithm: Resampling (connection to Doerry’s publication)
After uniformly sampling in , the data samples in are changed since these are now sampled at the values of that make uniform. Therefore, we first solve for the new values:
We now implement a second 1D interpolation in along-track to these samples which result in uniform sampling in around the center of the aperture:
The values of to sample at are generally chosen to cover the same wavenumber domain extent as the original data samples. To determine these values, , is solved for in terms of the minimum and maximum values across all range lines.
Once the extent of the integer samples is determined, we find the that corresponds to each. Continued…

## Slide 20: Polar Format Algorithm: Resampling (connection to Doerry’s publication)
We want to find the such that:
Solving for :

## Slide 21: Polar Format Algorithm: IFFT2
Once the samples are uniformly sampled in and , the IDFT can be taken in each dimension which results in the final focused scene.

## Slide 22: PFA Steps: Deramp in time and space
distortion at this stage is the first step (note the slight curvature in the along-track dimension)

## Slide 23: PFA Steps: Resample
distortion in this example is hard to see…
Notes: k_x distortion in this example is hard to see at this stage

## Slide 24: PFA Steps: Resample
distortion in this example is hard to see… but it is there

## Slide 25: PFA Steps: Resample
and sampling at each step

## Slide 26: PFA Steps: IFFT2
SAR focused image

## Slide 27: PFA spot-size limitations
The spot-size is limited because we ignored spherical wavefront deviations relative to the scene center.
  It does take care of the spherical wavefront at the scene center!
  We can remove the residual video phase term after step 1.
We already discussed that deramping keeps the instantaneous bandwidth small
PFA's polar-to-rectangular mapping is a genuine 2-D remap, but in practice it is done as two separable 1-D passes (range, then azimuth/keystone). Fielded systems often avoid explicit interpolation almost entirely. The range pass can be absorbed by varying the chirp rate or ADC sample timing per pulse, and the azimuth pass is done with a chirp-z transform.

## Slide 28: PFA spot-size limitations
Example for 1200 m spot at 10km range. “Full size” means the 1200 m spot can be achieved.
Walter C. Carrara, Ron S. Goodman, and Ronald M. Majewski, Spotlight Synthetic Aperture Radar: Signal Processing Algorithms, 1995

## Slide 29: Example methods for extending the spot size
N. E. Doren, C. V. Jakowatz, Jr., D. E. Wahl, and P. A. Thompson, "General formulation for wavefront curvature correction in polar-formatted spotlight-mode SAR images using space-variant post-filtering," Proceedings of the International Conference on Image Processing (ICIP), 1997.
N. E. Doren, Space-Variant Post-Filtering for Wavefront Curvature Correction in Polar-Formatted Spotlight-Mode SAR Imagery, Sandia National Laboratories report SAND99-2706, 1999.
A. W. Doerry, Wavefront Curvature Limitations and Compensation to Polar Format Processing for Synthetic Aperture Radar Images, Sandia National Laboratories report SAND2007-0046, 2007.