## Slide 1: Time Domain Correlation (Back Projection) SAR Processor

## Slide 2: Pulse Compression: Chirp Signal
Transmit signal is: where , is bandwidth and is the pulse duration (dropping the “sub-pd” for today from )
Instantaneous phase is ?
Instantaneous frequency is ?

## Slide 3: Pulse Compression: Chirp Signal
What do the plots of phase and frequency look like?

## Slide 4: Pulse Compression: Cross-correlation
Transmit signal is:
Cross-correlation (xcorr.m) is:
Transmit Signal
Delayed by Correlation Signal

## Slide 5
Pulse Compression: Cross-correlation
Transmit Signal
Delayed Signal
Cross correlation
Integrand
(Transmit * Delayed Signals)
Phase of the integrand

## Slide 6: Pulse Compression: Matched Filtering
What is the matched filter in the frequency domain?
  The conjugate of the transmit signal’s Fourier transform

## Slide 7: Pulse Compression: Derive response for boxcar (rect) weighted chirp
Transmit signal is:
The matched filter impulse response (conjugation in frequency domain) is the transmit signal time reversed and conjugated in the time-domain:
Convolution is then:
Matched Filter
Transmit Signal (time reversed and delayed)

## Slide 8: Pulse Compression: Derive response for boxcar weighted chirps
Convolution
This is two rect functions sweeping past each other.

## Slide 9: Pulse Compression: Derive response for boxcar weighted chirps
Convolution
This is two rect functions sweeping past each other. One method is to break the integral into two parts. The first part handles t < 0 and the second part handles t >= 0:

## Slide 10: Pulse Compression: Derive response for boxcar weighted chirps
Manipulating complex exponentials gives:
Starting with the first integral:
Combine exponentials:

## Slide 11: Pulse Compression: Derive response for boxcar weighted chirps
Noting that the numerator is an expression minus its conjugate, as in A+jB – (A-jB) = 2jB and noting that the imaginary part of the complex exponential is the sine of the argument:
Cancelling and adding in some terms:
Noting the final term is a sinc function:

## Slide 12: Pulse Compression: Derive response for boxcar weighted chirps
Doing the same for the second integral:
Combining complex exponentials:
Following the same steps as before, the second integral becomes:

## Slide 13: Pulse Compression Output : Derive response for boxcar weighted chirps
For :
  Since , we have , so we can rewrite as:
For :
  Since , we have , so we can rewrite as:
W

## Slide 14: Pulse Compression: Side lobes
What are they?
And why do we care?

## Slide 15: Pulse Compression: Side lobes
Sidelobes from large-RCS targets with can obscure signals from nearby smaller-RCS targets.
  Time sidelobes are related to pulse duration, .
fb = 2 k R/c
fb

## Slide 16: Pulse Compression: Side lobes
Abrupt changes in one domain require power spread over a wide domain in the Fourier pair (e.g. Fourier pairs like time and frequency, space and wavenumber)
So what can we do?

## Slide 17: Pulse Compression: Low Sidelobe Applications
Time-domain Tukey windowing for small time bandwidth products where very low sidelobes are required and for lessening power amplifier distortion of the signal

## Slide 18: Pulse Compression: Low Sidelobe Applications
Importance of Tukey windowing for small time bandwidth products where very low sidelobes are required and for lessening power amplifier distortion of the signal

## Slide 19: Pulse Compression: Kaiser window

## Slide 20: Transmit Signal
The delayed by transmit signal is:
The delayed complex baseband signal from a delayed and demodulated transmit signal is:

## Slide 21: Matched Filter Signal
Matched filtered signal is:
Simplifying assumption: for :
Modulated, Delayed by , and then Demodulated:

## Slide 22: SAR Aperture Signal for Linear Flight Path
Geometry?
Range? ?

## Slide 23: SAR Aperture Signal for Linear Flight Path
Phase?
Frequency?

## Slide 24: Along-track resolution
Notes: Chris Allen’s slide

## Slide 25: Along-track resolution
Notes: Chris Allen’s slide

## Slide 26: Along-track resolution
Notes: Chris Allen’s slide

## Slide 27: Along-track resolution
Notes: Chris Allen’s slide

## Slide 28
Now solve for R and fD for all target locations and plot lines of constant range (isorange) and lines of constant Doppler shift (isodops) on the surface.
Along-track resolution
Notes: Chris Allen’s slide

## Slide 29: Along-track resolution
Isorange and isodoppler lines for aircraft flying north at 10 m/s at a 1500-m altitude. r = 2 m, V = 0.002 m/s, fD = 0.13 Hz @ f = 10 GHz,  = 3 cm
Notes: Chris Allen’s slide

## Slide 30: Strip-map SAR signal example (no squint)
Notes: Chris Allen’s slide

## Slide 31: 2D (time-space) correlation filter with a time-space varying filter for SAR processing
Just use the point target simulator to generate the matched filter coefficients for each image pixel!
  For loop to simulate a point target in each pixel in the SAR image
    Point target is in the middle of the pixel
  The value for that image pixel is the inner product between the simulated dataset (vector of data) and the measured dataset (vector of data)
    The inner product is a measure of similarity
    The inner product is identical to the correlation operation for one specific time and space lag
    The image pixel value will be a complex number

## Slide 32: Step 1: Create simulated dataset

## Slide 33: Step 2: Create an image matrix (slant plane or ground plane)

## Slide 34: Step 2: For each pixel in the image matrix, compute the scattering simulation for a point target located in the center of the pixel

## Slide 35: Step 3: Take the inner product of the measurement and the simulated image pixel. Put the resultant value in the image pixel. Move onto the next image pixel.

## Slide 36: Step 4. Frequency-Wavenumber (f-kx) domain windowing for sidelobes

## Slide 37: SAR Analysis

## Slide 42: VERY SLOW: How can we speed this up?

## Slide 43: VERY SLOW: How can we speed this up?

## Slide 44: 2D Matched Filter
Needs to behave like convolution
Linear invariant filter coefficients
  But inner product coefficients using simulator do have a term that varies
  We need to normalize the filter components (weights) to one of the components in the filter.
  Choose the pixel which corresponds to the range of closest approach
  Red term is the problem – depends on absolute which is not relative to the current pixel/time !!!

## Slide 45: 2D Matched Filter
Needs to behave like convolution
Linear invariant filter coefficients
  But inner product coefficients using simulator do have a term that varies
  We need to normalize the filter components (weights) to one of the components in the filter.
  Choose the pixel which corresponds to the range of closest approach
  Red term makes this a bad… now fixed since it only removes phase offsets relative to the current pixel/time, !!!

## Slide 46: Resampling
Two algorithms or tools that we will need:
  Non-uniform sampling of uniformly sampled data
  Sampling of non-uniformly sampled data
How can we do this?

## Slide 47: Interpolation of Band Limited Signals
We are specifically interested in SAMPLED Band Limited Signals where we want to know a value between currently known samples.
Applications
  Time domain correlation when pulse compression is used.
  Resampling for analyzing SAR processor performance
  Range cell migration correction in the RDA
  Stolt interpolation in FK migration
  Resampling SAR images as part of a co-registration process
  Geocoding SAR imagery or re-projecting into different map coordinates

## Slide 48: Interpolation of Band Limited Signals: Quick thought experiment
Pretend you are only allowed to know the value of a continuous signal at one point (e.g. where you will sample it)
If you could first apply the Fourier time shift property to the signal with a time shift of that you controlled, then you could find the value at any other point offset by from the sampling point:
This is one way to think about band-limited interpolation… we delay the signal to the positions where are samples lie.

## Slide 49: Interpolation of Band Limited Signals: Sampled signal

## Slide 50: Interpolation of Band Limited Signals: Reconstruct and delay

## Slide 51: Interpolation of Band Limited Signals: Resample this reconstructed and delayed signal
If we resample this “convolution with a delayed sinc”, this is:
Simplifying, we find that it is just convolution with the sampled and delayed sinc function:

## Slide 52: Interpolation of Band Limited Signals: Non-uniform sampled data
The sinc kernel can be extended to interpolating non-uniformly sampled data. Since the sinc function is analytical, we just need to sample it at the point locations that we have available to us.
This can be used to re-sample data from platforms with varying velocity. If the PRF is constant, the azimuth sampling will be variable in space. By resampling at uniform positions, we can make use of FFT based algorithms.