## Slide 1: Thwaites MELT Accumulation Radar
John Paden, Fernando Rodriguez, Carl Robinson, Alejandra Escalera, Richard Hale, Krishana Karidi, Cameron Lewis, Bradley Schroeder, Jiaxuan Shang, Hara Talasila, Tom Jordan, Keith Nichols
Center for Remote Sensing of Ice Sheets, University of Kansas, Lawrence, USA
British Antarctic Survey, Cambridge, UK
July 12, 2019

## Slide 2: Accumulation Radar
Accumulation rate is a key variable in interpreting surface elevation measurements and in determining the mass input
600-900 MHz frequency
  Large bandwidth and smaller antenna size
  Disadvantage due to increased ice attenuation, increased ice scattering leading to clutter and extinction, decreased conductive reflections

## Slide 3: Modifications
Compact size:
  30 lbs electronics, single 3U 19” rack box
Increased transmit power: 400 W
Shielded housing for antenna
Calibration loop for amplitude/phase monitoring with transmit path

## Slide 4: Block Diagram

## Slide 5: a) Anechoic Chamber b) Installed on BAS TO

## Slide 6: Installed on BAS Twin Otter
3U mid-depth chassis
5.25” x 19” x 18.5”
30 lbs electronics
28 VDC aircraft power
Red box is accumulation radar

## Slide 7: Issue…

## Slide 8: Issue…

## Slide 9: Pulse Compression
Echogram
A-scope
(single column marked in red)

## Slide 10: Time-Frequency Polynya
Time-frequency analysis over sea ice polynya
Third harmonic aliasing on transmit?
Raw data shows odd envelope at end of pulse

## Slide 11
Acknowledgements
The radar data used in this work were collected as a part of the NSF-NERC Thwaites Initiative. The radar system and SAR processing software were developed with support from the University of Kansas, NSF grant ANT-0424589, and NASA Operation IceBridge grant NNX16AH54G. We also acknowledge the contributions of many CReSIS faculty, staff, and students who contributed to the radar system development and to the BAS aircraft operations team for flying and supporting the mission.
THANK YOU!
QUESTIONS?